## Slide 1
Network Simulation
Al Mustafa University College
Computer Technology Eng. Dep.
By
Asst. Lect. Omer W. Taha
Lecture 6

## Slide 2: Subnets
Network Layer
4-51
IP address:
–subnet part - high order
bits
–host part - low order bits
what’s a subnet ?
–device interfaces with same subnet part of IP address
–can physically reach each other without intervening router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.1.4 223.1.2.9
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 3: Subnets
Network Layer
4-52
recipe
to determine the subnets, detach each interface from its host or router, creating islands of isolated networks
each isolated network is called a subnet
subnet mask: /24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.1.4 223.1.2.9
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 4: Subnets
Network Layer
4-53
how many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2

## Slide 5: Basics of Sub-netting
54
Classical IP addressing
Subnetworks
Subnet mask
Boolean operations: AND, OR, and NOT
Performing the AND function

## Slide 6: Subnetworks
55
To create a subnet address, a network administrator borrows bits from the original host portion and designates them as the subnet field.

## Slide 7: Subnetworks
56

## Slide 8: Subnet work
7 Application
6 Presentation
5 Session
4 Transport
1 Physical
2 Data Link
3 Network
Subnets
The Internet is running out of IP address. One solution
is to subnet a network address.
This is done by borrowing host bits to be used as
network bits.
Example:
Class B mask 255.255.0.0
Borrowing 1 bit gives a subnet mask of 255.255.128.0 Borrowing 2 bits gives a subnet mask of 255.255.192.0 Borrowing 3 bits gives a subnet mask of 255.255.224.0 Borrowing 4 bits gives a subnet mask of 255.255.240.0

## Slide 9: Subnet work
7 Application
6 Presentation
5 Session
4 Transport
1 Physical
2 Data Link
3 Network
Example:
Given an IP address of 180.200.0.0, subnet by
borrowing 4 bits.
Subnet mask = 255.255.240.0
The 4 bits borrowed are value 128, 64, 32, 16. This will create 16 sub networks, where the first and last will be unusable.
Sub network address:
180.200.0.0
180.200.16.0
180.200.32.0
180.200.48.0
180.200.64.0
etc…

## Slide 10: Subnet work
7 Application
6 Presentation
5 Session
4 Transport
1 Physical
2 Data Link
3 Network
The first 3 usable sub networks are:
180.200.16.0
180.200.32.0
180.200.48.0
For sub network 180.200.16.0, the valid IP address
are:
180.200.16.1 to 180.200.31.254
Directed broadcast address is:
180.200.31.255