## Slide 1
Asst. Lec. Lubna A. Alnabi
Analog to Digital Converters
Electronic branch
Fourth Class
Interface Circuits Design

## Slide 2: Analog to Digital Converters
What is Analog to Digital Converters (ADC)?
(ADC) are an electronic integrated circuit (IC) which transforms a signal from analog to digital form.

## Slide 3: Analog to Digital Converters
Why ADC is needed?
All microprocessors works with digital signal so ADC Provides a link between the analog and the digital worlds of signal processing.

## Slide 4: Analog to Digital Converters
What is ADC classification ?
1) The first group includes SAR, and flash-type converters.
2) The second group includes integrator and voltage to frequency converters.

## Slide 5: Analog to Digital Converters
What is the tradeoff between ADC groups?
Accuracy
Speed

## Slide 6: Analog to Digital Converters
What is the uses of ADC (successive- approximation and the Integrator)?
successive-approximation is used as data loggers
The integrator types are
used as digital meter

## Slide 7: Analog to Digital Converters
What is ADC process?
Sampling and Holding
Quantizing and Encoding

## Slide 8: Analog to Digital Converters

## Slide 9: Analog to Digital Converters
Sampling and Holding:-
It is a process of taking a sufficient number of discrete values at point on a waveform that will define the shape of waveform.

## Slide 11: For a 3 bit A/D, with Vmin=0 V, V max=10 V, what is the code-word for Vin=5.7 Volts?

## Slide 13: Analog to Digital Converters
Resolution:-
Resolution is the number of bits used for conversion (8 bits, 12 bits, …)

## Slide 14: Analog to Digital Converters
How to increase Accuracy of A/D Conversion?
Increasing the resolution
Increasing the sampling

## Slide 15
Flash A/D Converter
What is flash A/D Converter Components
Resistors use the resistors to form a ladder voltage divider
2) Comparators comparing input signal to reference voltage.
3) Priority encoder produces a binary output.

## Slide 16: Find the code-word for a 3 bit, flash A/D with Vref=8V with Vin=5.6V.

## Slide 17: How does Flash A/D work?
1- Vref is divided over the resistors
2- The voltage on the resistors is compared with Vin
3- The output of the comparator is fed to the priority encoder.

## Slide 18: What is sigma delta A/D Converter Components draw the CCT
1- Adder
2- Integrator
3- Comparator
4- D/A

## Slide 19: Find the code-word for a 4 bit, sigma-delta A/D with Vref=2.5V with Vin=1.1V.

## Slide 20: How does dual slope work?
1- Control Logic switches to Vin and starts the counter.
2- Charging starts and lasts for Tch.
3- Control logic Switches to -Vref and restart the counter.
4- Discharge for Tdis until reaches the threshold and Enable output latch.

## Slide 21: What is dual slope A/D Converter Components draw the CCT
Integrator
Electronically Cont
Counter
Clock
Control Logic
Comparator

## Slide 22: What is SAR A/D Converter Components draw the CCT
1Comparator
2- SAR unit
3- DAC
4- Output Register

## Slide 23: Find the code-word for a 5 Bit SAR A/D with Vin=0.6V while Vref=1V.
MSB (bit 5)
Vref /2
If Vin > than Vref /2 , turn MSB on (1)
If Vin < Vref /2 , turn MSB off (0)
Vin =0.6V and V=0.5
Since Vin>V, MSB = 1 (on)
 |  |  |  | 1

## Slide 24
Next Calculate (bit 4)
V=Vref/2 + Vref/4= 0.5+0.25 =0.75V
Since Vin < 0.75, bit 4= 0
(bit 3)
V=Vref/2(0.5) + Vref/8 =0.625
Since 0.6<0.625, MSB is turned off bit 3 = 0
(bit 2)
V=Vref/2(0.5) + Vref/16 =0.5625
Since 0.6>0.5625 MSB is turned off bit 2 = 1
(bit 2)
V=0.5625 + Vref/32 =0.59375
Since 0.6>0.59375 MSB is turned off bit 2 = 1
1 | 1 | 0 | 0 | 1