## Slide 1
Asst. Lec. Lubna A. Alnabi
Electronic branch
Fourth Class
Interface Circuits Design
Centronic Port

## Slide 2: Centronic Port
The Centronic port, also known as the printer port or the parallel port, is an industrial standard interface designed for connecting printers to a computer. A computer at least has one such a port installed. The port may come with the computer's mother-boards or with plug-in I/O cards. Adding more Centronic ports is easy and inexpensive. In total, four Centronic ports may be installed on a computer and they have logic names LPT1 to LPT4.

## Slide 3: Centronic Port
Mother boards have 1, adding more is easy and inexpensive using
plug in I/O cards (Max.4)
They have Logic name (LPT1 to LPT4)
Work with distance < or= 5 meters

## Slide 4: Centronic Port
The port connectors on a computer and on a printer are different. The one on the computer is a 25 pin D-type female connector , and the latter is a 36pin female Centronic-type connector (Figure 1.1(b)). The pin functions of the two connectors. To connect a printer to a computer, a printer cable is used . The length of the cable must not exceed 5 meters. The Centronic interface is not for long distance operations.

## Slide 5: Centronic Port
Groups (Data, Control and Status):-
The I/O lines in the port are organized into three groups, namely, the Data group, the Control and the Status group.

## Slide 6: Centronic Port
Data group
This sends data from PCs to external devices. It has eight latched output lines and the
group is associated with an 8-bit CPU port. The address is: base address.
Control group
This controls the operation of external devices. It contains four latched output lines (STROBE,
-LF/CR, -SLIN and -INITIALIZE) which are from the computer to the
devices. The group is controlled by a CPU port having an address: base address+2. STROBE,
-LF/CR And -SLIN lines Are inverted.-INITIALIZ is not.
Status group
The group is used by the computer to obtain the current status of external devices. It
contains five lines (-ERROR, SLCT, PE,-ACK and BUSY), which are directed from
external devices to the computer. It is fed into a CPU port, the address of which is:
base address+l. BUSY line is inverted and the other four lines are not.