## Slide 1
Image Processing
المرحلة الرابعة
Tenth lecture
by
Assit.Lec. Shaimaa Shukri

## Slide 2
Chapter_ Two
Image Analysis
Algorithms and solved questions
Q/ Algorithm 1: Enlargement Digital Image using Zero_Order Hold.
Input: Image File (NxN) Output :ImageFile(2Nx2N) Step1 :N=0:M=0
Step 2: For I = 2 to width of input image -1 For J = 2 to height of input image-1
For each Picture1.point (Pixel) do the following: Red = Pixel (I, J) Mod 256
Green = ((Pixel(I,J) And &HFF00FF00) / 256 &)
Blue
= ((pixel (I, J) And&HFF0000) / 65536)
If Red<0 then Red =0
If Red>=255 then Red =255 If Green<0 then Green =0
If Green>=255 then Green=255 If Blue<0 the Blue =0
If Blue>=255 then Blue=255
Draw Picture2.PSet (N,M), RGB(Red, Green, Blue) M=M+1
Draw Picture2.PSet (N,M), RGB(Red, Green, Blue)
Next J
N=N+1
For K = 1 to M
A= Picture2.Point(N - 1, K)
Draw Picture2.PSet (N,K), A
Next K M=0 N=N+1
Next I

## Slide 3
Chapter_ Two
Image Analysis
Q/ Sobel Edge Detection Algorithm
Input: Gray level Image File, Image Width, Image Height, Column
Mask, Row Mask
Output: Edge Image File.
Step1: Set the counters, Row and Column to one.
Step2: Cut the window size (3X3) from the original image, such that the central pixel of the window is the pixel in the original image
whose location (Row, Column)
Step3:
1 1
perform the convolution process as follows:
convolve the window two times , first convolved it with row mask, second convolved it with column mask as described in the following equation:
Temporary-image (x, y) = window(i, j) * mask(i, j)
i1i1
Where the result of the two convolutions are S1 and S2.
Perform the following equation to obtain the edge magnitude :
Edge Magnitude =
1 2
S 2  S 2
Store the result in edge _image location (Row, Column).
Shift the window one pixel to the right of the original –image by increment column by one.
Step4: If column = width -1 then go to step 5 Else repeat steps (2), (3) and (4)
Step5: Move the window image one Row down in original Image.
Step6: Repeat step (3) until Row=Height -1, Column= Width -1.

## Slide 4
Chapter_ Two
Image Analysis
Q/ Enlarge the following sub image using:
Zero_Order Hold method
First _Order Hold method
1. Zero_Order Hold
30 | 30 | 40 | 40 | 100 | 100 | 40 | 40
30 | 30 | 40 | 40 | 100 | 100 | 40 | 40
40 | 40 | 40 | 40 | 80 | 80 | 80 | 80
40 | 40 | 40 | 40 | 80 | 80 | 80 | 80
10 | 10 | 50 | 50 | 50 | 50 | 90 | 90
10 | 10 | 50 | 50 | 50 | 50 | 90 | 90
2. First _Order Hold method
80
90
Q/ Apply a median filter (Order Statistic) on the following assumed image, using (3×3) Window size:
0
30 40 100 40
40 40 80 80
10 50 50 90
20 | 44 | 56 | 100 | 90 |  |  |  |  |  | 
37 | 45 | 55 | 200 | 90 |  |  |  |  |  | 
22 | 80 | 100 | 100 | 50 |  |  |  |  |  | 
20 | 90 | 200 | 200 | 100 |  |  |  |  |  | 
20 | 33 | 210 | 180 | 230 |  |  |  |  |  | 
22 | 80 | 100 | 100 | 150 |  |  |  |  |  | 
 |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 
 |  |  |  |  | 0 | 45 | 80 | 90 | 0 | 
Solution |  |  |  | 0 |  | 55 | 100 | 100 |  | 0
 |  |  |  | 0 |  | 80 | 100 | 180 | 0 | 
 |  |  |  | 0 |  | 80 | 100 | 180 |  | 0
 |  |  |  | 0 |  | 0 | 0 | 0 |  | 0