## Slide 1: Serial to Parallel and Parallel to Serial
ITC 232
It is a peripheral chip which is designed for easy interfacing with
the RS232 port on computers
It is connected to the RS232 port via three lines, TD, RD and ground
It is a peripheral chip which is designed for easy interfacing with
the RS232 port on computers

## Slide 2: Serial to Parallel and Parallel to Serial
ITC 232
Users can input command from keyboardy, there is no need for users to learn low-level languages and hardware
controls
ITC 232
1) The IC has 24 I/O lines arranged in three ports A, B and C.
2) put. Bits 4 to 7 of portsA, B and C can be used to drive 3PH stepper motors
3) Bits 0 to 3 of ports A, B and C can be used to measure resistance or capacitance

## Slide 3: Serial to Parallel and Parallel to Serial
ITC 232/ The ITC232-A has a 40-pin. The device requires a +5V power supply and consumes 50 mA. The RS232 serial I/O command port operates with a baud rate from 300 to 115, 200.

## Slide 4: Serial to Parallel Interface
By using serial-in and parallel-out shift registers such as the 74LS164s, two output lines from a computer can generate an unlimited number of outputs. 74LS164 is used to generate eight output lines from two output lines of a PC. The 74LS164 has two serial data inputs, pins 1 and 2 (A and B) and
eight shift register outputs (Qa to Qh)

## Slide 5: Serial to Parallel Interface
there are two problems associated with the serial-to-parallel interface. One is the data transfer rate. A Pentium computer can output clock signal at a frequency in the range from 0.1 MHz to 1 MHz. The more outputs you have in the circuit, the slower the loading speed is. This is not a problem for low and medium speed interfacing applications. The other problem is that during data loading, the output same times changes randomly. To solve this, data latches such as the 74LS374 can be used

## Slide 6: Parallel to Serial Interface
Using a parallel-in and serial-out shift register such as the CD4021, the number of inputs to a computer can be expanded. It requires two output lines from the computer (one to load parallel data and one to shift the data) and one input line to the computer to read data.