## Slide 1: 2018-2019
رهاط ةزمحلا .م : ةداملا سردم
Dr. Hussam Dheaa Kamel
Al-Mustafa University Collage CTE Department 2018-2019
Digital Communications
CTE Department -3rd stage
Reference: Digital Communications Fundamentals and Applications,
2nd Addition, by FernardSklar

## Slide 2
Digital Communications
CTE Department -3rd stage
Example 1:
A television signal with bandwidth of 4.2 MHz is transmitted using binary PCM. The number of quantizatin levels is 512. Calculate:
Code word length
Transmission bandwidth iii- Final bit rate
iv- Output signal to quantization noise ratio
Solution:
i- 𝑞 = 2𝑣 → 512 = 2𝑣
𝑙𝑜𝑔512 = 𝑣 × 𝑙𝑜𝑔2 = 9 𝑏𝑖𝑡𝑠
Thus the code word length is 9 bits
ii- 𝐵𝑇 ≥ 𝑣𝑊 → 𝐵𝑇 ≥ 9 × 4.2 × 106
∴ 𝐵𝑇 ≥ 37.8 𝑀𝐻𝑧

## Slide 3
Digital Communications CTE Department -3rd stage
iii- The signaling rate 𝑟 = 𝑣 × 𝑓𝑠 = 𝑣 × 2𝑊 = 9 × 2 × 4.2 × 106
𝑟 = 75.6 𝑀𝑏𝑝𝑠
1
𝑁
Also we have 𝐵𝑇 ≥ 2 𝑟 𝑜𝑟 𝐵𝑇 ≥ 0.5 × 75.6 = 37.8 𝑀𝐻𝑧 which is same value obtained earlier
iv- (𝑆 ) 𝑑𝐵 = (4.8 + 6𝑣)𝑑𝐵 = 4.8 + 6 × 9 = 58.8 𝑑𝐵
Example 2:
The bandwidth of signal input to the PCM is restricted to 4 kHz. The input varies from -3.8V to +3.8 V and has the average power of 30 mW. The required signal to noise ratio is 20 dB.
iii-
Calculate the number of bits required per sample.
Outputs of 20 such PCM coder are time multiplexed. What is the mimum required transmission bandwidth for the multiplexed signal?
What is the signaling rate for the multiplexed signal?
Solution:
𝑆
(𝑁) 𝑑𝐵 = 10𝑙𝑜𝑔
10
𝑆
𝑁
( ) 𝑑𝐵 = 20𝑑𝐵
∴
𝑁
𝑆 = 100

## Slide 4
Digital Communications
CTE Department -3rd stage
i-
𝑆 = 3𝑃 × 22𝑣 → 100 = 3×30×10−3×22𝑣
𝑁 (𝑥2 ) (3.8)2
𝑚𝑎𝑥
22𝑣 = 1444 = 24066.67
0.06
2𝑣𝑙𝑜𝑔2 = log(24066.67)
𝑣 ≅ 7 𝑏𝑖𝑡𝑠
ii- 𝐵𝑇 ≥ 𝑣𝑊 and for 20 multiplexed signals
𝐵𝑇 ≥ 20 × 7 × 4 𝑘𝐻𝑧 ≥ 840 𝑘𝐻𝑧
iii-
The signaling rate
𝑟 = 2𝐵𝑇 = 2 × 840 = 1680 𝑘𝑏𝑝𝑠

## Slide 5
Digital Communications
CTE Department -3rd stage
Example 3:
The information in an analog signal voltage waveform is to be transmitted over a PCM system with an accuracy of
∓0.1% (full scale). The analog signal has a bandwidth of 100Hz and an amplitude range of -10 to +10 volts. Determine:
i- The number of levels required for such accuracy. ii- The code word length.
The minimum bit rate required.
The bandwidth required for PCM signal.
Solution:
i- The maximum quantization error should be ∓0.1%, so:
𝜀𝑚𝑎𝑥 = ∓0.001
𝛿
But 𝜀𝑚𝑎𝑥 = |2|
𝛿
|2| = 0.001 → 𝑡ℎ𝑒 𝑠𝑡𝑒𝑝 𝑠𝑖𝑧𝑒 𝛿 = 0.002

## Slide 6
Digital Communications
CTE Department -3rd stage
𝑞
We have 𝛿 = 2𝑥𝑚𝑎𝑥 , 𝑎𝑛𝑑 |𝑥𝑚𝑎𝑥| = 10 𝑣𝑜𝑙𝑡𝑠
Then 0.002 =
2×10
𝑞
→ 𝑞 = 10000
So that the number of levels are 10000.
ii- We have 𝑞 = 2𝑣 → 10000 = 2𝑣 → 𝑙𝑜𝑔10000 = 𝑣 𝑙𝑜𝑔2
∴ 𝑡ℎ𝑒 𝑐𝑜𝑑𝑒 𝑤𝑜𝑟𝑑 𝑙𝑒𝑛𝑔𝑡ℎ 𝑣 = 13.288 ≅ 14 𝑏𝑖𝑡𝑠
iii-
We have the bit rat 𝑟 = 𝑣𝑓𝑠 = 𝑣 × 2 × 𝑊 = 14 × 2 × 100 = 2800 𝑏𝑝𝑠
1 1
iv- The bandwidth required 𝐵𝑇 ≥ 2 𝑟 ≥ 2 × 2800 = 1400 𝐻𝑧

## Slide 7
Digital Communications
CTE Department -3rd stage
H.W:
Q1/ The information in an analog waveform with maximum frequency 𝑓𝑚 = 3 𝑘𝐻𝑧 is to be transmitted over 16- levels PCM system. The quantization distortion is specified not exceed 1% of peak to peak analog signal.
i-
ii-
What is the number of bits per sample that should be used in this PCM? What is minimum bit transmission rate?
Q2 / A signal of bandwidth 3.5 kHz is sampled, quantized and coded by PCM system. The code signal is then transmitted over a transmission channel of supporting a transmission rate of 50 kbps. Calculate the maximum signal to noise that can obtained by this system. The input signal has peak to peak value of 4 volts and rms value of 0.2 V.
Q3 / Consider an audio signal comprised of the sinusoidal term 𝑠(𝑡) = 3 cos(500𝜋𝑡).
i- Find the number of quantization level with an accuracy of 1%. ii- Determine the signaling rate.
iii- The bandwidth of transmission channel.

## Slide 8
Digital Communications
CTE Department -3rd stage
  Advantages of PCM:
    Effect of channel noise and interference is reduced.
    PCM permits regeneration of pulses along the transmission path. This reduces noise interference. iii- The bandwidth and signal to noise ratio are related by exponential law.
Multiplexing of various PCM signals is easily possible.
Encryption or decryption can easily incorporated for security purpose.
  Limitation of PCM:
    PCM system are complex compared to analog pulse modulation method.
    The channel bandwidth is also increased because of digital coding of analog pulses.
  Modifications of PCM:
    PCM can be modified to delta modulation. It is more simplified method of implementation.
    The PCM can be used in wideband communications channels to overcome the bandwidth problem.
    With the help of data comparison along with PCM, the redundancy can be removed and data rate can be reduced.